## Slide 1
Tuning Target Delay for RTT-based Congestion Control
Jian Tang, Tingting Xu, Camtu Nguyen, Xiaoliang Wang, Sanglu Lu and Baoliu Ye
Nanjing University

## Slide 2
Background
Remote Direct Memory Access (RDMA)
High Throughput: 100Gbps or higher
Ultra-low latency: a few µs with a rack
Low CPU overhead:
Offload stacks at hardware
  Avoid memory copy
  Bypass the local kernel/remote CPU.
Machine A
DMA
ram
cpu
rnic
Machine B
DMA
ram
cpu
rnic
Network

## Slide 3
Background
Remote Direct Memory Access (RDMA)
High Throughput: 100Gbps or higher
Ultra-low latency: a few µs with a rack
Low CPU overhead:
Offload stacks at hardware
  Avoid memory copy
  Bypass the local kernel/remote CPU.
Machine A
DMA
ram
cpu
rnic
Machine B
DMA
ram
cpu
rnic
Network

## Slide 4
Background
Remote Direct Memory Access (RDMA)
High Throughput: 100Gbps or higher
Ultra-low latency: a few µs with a rack
Low CPU overhead:
Offload stacks at hardware
  Avoid memory copy
  Bypass the local kernel/remote CPU.
Machine A
DMA
ram
cpu
rnic
Machine B
DMA
ram
cpu
rnic
Network

## Slide 5
Background
Remote Direct Memory Access (RDMA)
High Throughput: 100Gbps or higher
Ultra-low latency: a few µs with a rack
Low CPU overhead:
Offload stacks at hardware
  Avoid memory copy
  Bypass the local kernel/remote CPU.
Machine A
DMA
ram
cpu
rnic
Machine B
DMA
ram
cpu
rnic
Network

## Slide 6
Background
In past, RDMA deployed on special fabrics, i.e., InfiniBand.
- incompatible with Ethernet + IP

## Slide 7
Background
In past, RDMA deployed on special fabrics, i.e., InfiniBand.
- incompatible with Ethernet + IP
Routable RDMA over Converged Ethernet (RoCEv2)
Ethernet
IP
UDP
InfiniBand L4
Payload
-Efficient but requires a lossless fabric for optimal performance
*packet format

## Slide 8
Background
In past, RDMA deployed on special fabrics, i.e., InfiniBand.
- incompatible with Ethernet + IP
Routable RDMA over Converged Ethernet (RoCEv2)
Ethernet
IP
UDP
InfiniBand L4
Payload
-Efficient but requires a lossless fabric for optimal performance
Priority-based Flow Control (PFC)
- simple but ... victim flows 、dead lock、head of line blocking
*packet format

## Slide 9
Background
In past, RDMA deployed on special fabrics, i.e., InfiniBand.
- incompatible with Ethernet + IP
Routable RDMA over Converged Ethernet (RoCEv2)
Ethernet
IP
UDP
InfiniBand L4
Payload
-Efficient but requires a lossless fabric for optimal performance
Priority-based Flow Control (PFC)
- simple but ... victim flows 、dead lock、head of line blocking
RoCEv2 needs congestion control
  Avoid PFC frames 、Provide low latency、Achieve high link utilization
*packet format

## Slide 10
Background
RTT-based Congestion Control for Datacenters
Fine-grained informative
End-to-end metric
Good applicability in datacenters
  Predicable topology
  Accurate RTT measurements in hardware
#TIMELY (SIGCOMM 2015), DX (ATC 2015), ROGUE (SoCC 2018), SWIFT (SIGCOMM 2020)

## Slide 11
Motivation
Core algorithm in RTT-based congestion controls
(1)
(2)
Target
Decrease speed
Increase speed

## Slide 12
Motivation
Core algorithm in RTT-based congestion controls
(1)
(2)
Target
Decrease speed
Increase speed
How to configure the target value

## Slide 13
Motivation
40 : 1 incast with different target
Low target => Low bandwidth
High target => High latency

## Slide 14
Motivation
40 : 1 incast with different target
2/20/100 : 1 incast with static target
Low target => Low bandwidth
High target => High latency
A static target does not apply
to all trafﬁc patterns !

## Slide 15
Motivation
Optimal target increases as the number of flows
More flows

## Slide 16
Motivation
Optimal target increases as the number of flows
More flows
Complexity

## Slide 17
Motivation
Optimal target increases as the number of flows
More flows
Less queue stability
Complexity

## Slide 18
Motivation
Optimal target increases as the number of flows
More flows
Complexity
Less queue stability
Large target for more headroom

## Slide 19
Goal
Accurate target value for RTT-based CC
  Provide the lowest target with guaranteed bandwidth
  Automatically update according to the traffic pattern
2. Easy to deploy
  No switch modification needed
3. Easy to configure
  Few & independent parameters

## Slide 20
Observation
Port utilization keeps the same under different workloads!
Large Small Optimal
100% ~95% 95%~99%

## Slide 21
Observation
Port utilization keeps the same under different workloads!
Large Small Optimal
Instant port utilization is a good indicator
100% ~95% 95%~99%

## Slide 22
Solution
Update the target according to the queue status
Port Utilization > η: target
Port Utilization < η: target e.g. η=99%

## Slide 23
Solution
Challenge #1 How to obtain the queue status?
Switch
Queue Length > 0 => ECN:1
No hardware modification
No complicated ECN parameter tunning problem
Receiver
ECN mark ratio

## Slide 24
Solution
Long Feedback Delay
Sender
ACK & ECN marking ratio
Message
Target update
Feedback are separated
Challenge #2 Where to update the target?

## Slide 25
Solution
Switch
Queue Length > 0 => ECN:1
Receiver
ECN mark ratio
Target update
Target
Challenge #2 Where to update the target?

## Slide 26
Sender (RP)
Window
Update
Switch (CP)
ECN Flag
Receiver (TGP)
Target
Update
Target
Overall Design
Message
Message
Target
Target generation module (TGM)
Reaction Point (RP) : sending hosts
Congestion Point (CP) : congested switch
Target Generating Point (TGP) : receiving host

## Slide 27
RET Congestion Control
Reaction Point (RP) based SWIFT Google 2020
  AIMD controller based on whether the measured queuing delay exceeds target

## Slide 28
RET Congestion Control
Congestion Point (CP)
  Traditional ECN marking method with threshold “zero”
Reaction Point (RP) based SWIFT Google 2020
  AIMD controller based on whether the measured queuing delay exceeds target

## Slide 29
RET Congestion Control
Congestion Point (CP)
  Traditional ECN marking method with threshold “zero”
Target Generation Point(TGP)
  Switch ECN flag:
    0: target + δ
    1: target - (1- η) * δ e.g. η = 99%
Reaction Point (RP) based SWIFT Google 2020
  AIMD controller based on whether the measured queuing delay exceeds target

## Slide 30
RET Congestion Control
Time
Queue size
large target
high marking Ratio
target drops
marking ratio ≈ η

## Slide 31
RET Congestion Control
Time
Time
Queue size
Queue size
large target
high marking Ratio
target drops
marking ratio ≈ η
small target
low marking ratio
target rises
marking ratio ≈ η

## Slide 32
RET Congestion Control
Simple & Effective
Slow Reaction
RP algorithm optimization
Target Approach (Swift 2020)
(1)

## Slide 33
RET Congestion Control
Simple & Effective
Slow Reaction
RP algorithm optimization
Target Approach (Swift 2020)
Gradient Approach
Fast Reaction
(1)
(2)

## Slide 34
RET Congestion Control
Simple & Effective
Slow Reaction
RP algorithm optimization
Target Approach (Swift 2020)
Gradient Approach
Fast Reaction
How to avoid gradient approach takes RTT spikes as congestion signal?
(1)
(2)

## Slide 35
RET Congestion Control
|Gradient| > target
Target Approach
Gradient Approach
ACK & Target
Using target to filter the RTT noisy
RP algorithm optimization

## Slide 36
Evaluation
RET ensures fairness between different flows
Multiple senders and one receiver
Change the number of flows every 20 ms

## Slide 37
Experiment
RET provides better target for various traffic pattern
Timlely: 2015
DCQCN: 2015
DX: 2015
RDMA-SWIFT: 2020
63 sending hosts and one receiving host
Monitor queue size and system throughput for different incast ratio

## Slide 38
Experiment
Gradient approach causes better stability and convergence
Two sending hosts, each initiate 20 flows to the same receiving host at line rate

## Slide 39
Experiment
RET provides shortest FCT among tested protocols
Large-scale simulation
Leaf-spine: 288-hosts, 12 Leafs and 6 Spines
Web-server & Hadoop

## Slide 40
Limitation
Assumption: Congestion occurs primarily at host downlinks
CONGA (2014) MP-RDMA (2018) SRD (2020)

## Slide 41
Related Work
Timely SIGCOMM2015
  Unfairness, instability
DX/ ROGUE ATC 2015/SOCC 2018
  Low throughput
DCQCN SIGCOMM2015
  Complicated ECN parameter tunning
SWIFT SIGCOMM2020
  Low throughput or High latency

## Slide 42
Conclusion
The setting of target for RTT-based congestion control.
First effort targeting at achieving accurate target value in realtime.
Integrate our target generation module into SWIFT
Compared with tested protocols, RET provides better performance

## Slide 43
THANKS & QUESTIONS ?
tangjian@smail.nju.edu.cn